Information Gathering On RFID Reader/tag

==>In our project we need RFID module which can communicate with multiple
       tag or cards.
==>For that RD522 RFID module is best which is multi-communication RFID
      module for arduino or any other micro-controller.
==>Also known as MFRC-522 due to its NFX semiconductor. The module allows
       developers to interface with any SPI, I2C and UART based microcontroler.
==>Its work on 13.56 MHz frequency. The RFID cards communicate with the
       module at a short distance with radio frequency due to the mutual induction
       technique.
==>The RFID cards and reader (RC522) can transfer data up to 10Mb/s.

### Power/Reset Pins
PINS		DETAILS
Pin 1	VCC	The power pins are VCC. In some versions of RC522, this pin is denoted by 3V3 on the module instead of VCC.
Pin 2	RST	It’s a reset pin for the module. Therefore, it uses to reset the device in case of an error on when a device isn’t giving any response.
Pin 3	Ground	Ground helps to make the common ground with every external device, e.g. power Supply, Microcontroller or Arduino.

### SPI and UART Communication Pins
PINS			DETAILS
Pin 4	IRQ		The device can go into sleep mode to save power. So, the IRQ helps to wake it.
Pin 5	MISO	SCL / TX	This pin connects with the Arduino/Microcontrollers for SPI communication. However, it transfers the data from module to Arduino. / The MISO pin is also useable for other functions instead of SPI. / It can also interface with I2C for clock pulse and UART Serial for Data transfer from the module.
Pin 6	MOSI		MOSI is the data input pin for RFID module in SPI communication
Pin 7	SCK		The SCK pins help to send the clock pulse in SPI communications.
Pin 8	SS	SDA / RX	The SS pin is a chip enable pin in SPI communication. Therefore, it receives the signal when Master (Arduino) must perform SPI communication. / The SS pin in RFID is useable as a second pin (SDA) for I2C communication. / It also receives data during UART communication.

Required Library to program RFID and Important steps:

#include <SPI.h>
>>>>>>>>>establish the SPI communication

#include <MFRC522.h>
>>>>>>>>helps to decode and encode the incoming data from the RFID module

NOTE : These two libraries are dependent on each other

---------------------------------------------------------------------------------------------------

MFRC522 mfrc522(SS_PIN, RST_PIN);
>>>>>>>>>>describe the reset and slave select (SS) pin
>>>>>>>>>>above command change the SS_PIN with Slave select and RST_PIN
        with reset pin of the RFID

---------------------------------------------------------------------------------------------------

SPI.begin();
mfrc522.PCD_Init();
>>>>>>>>>>describe the SPI initialization and Module initialization

----------------------------------------------------------------------------------------------------------------------------

mfrc522.PICC_IsNewCardPresent()
>>>>>>>>>>>Detect the card
mfrc522.PICC_ReadCardSerial()
>>>>>>>>>>read the data

NOTE : Sometimes the card can be present on the module but it has no data. Therefore, the second command ReadCardSerial will help to detect that
---------------------------------------------------------------------------------------------------
---------------------------------------------------------------------------------------------------

mfrc522.PICC_DumpDetailsToSerial(&(mfrc522.uid)); [decimal]
mfrc522.PICC_DumpToSerial(&(mfrc522.uid)); [HEX]
>>>>>>>>>>to see the dumb the data so it can decrypt

NOTE : the device can read and dump/decrypt the data of a single card at a time. Therefore, During Dumping the device won’t be able to read the new card.

---------------------------------------------------------------------------------------------------

MFRC522::StatusCode status //To read the status
mfrc522.PCD_Authenticate //To get the authentication
mfrc522.MIFARE_Read //To read the card
---------------------------------------------------------------------------------------------------
mfrc522.PICC_HaltA(); // Stop reading
mfrc522.PCD_StopCrypto1(); // Stop encryption on PCD
---------------------------------------------------------------------------------------------------

Write data into RFID tag

#include <SPI.h>
#include <MFRC522.h>S

constexpr uint8_t RST_PIN = D3; // Configurable, see typical pin layout above
constexpr uint8_t SS_PIN = D4; // Configurable, see typical pin layout above

MFRC522 mfrc522(SS_PIN, RST_PIN); // Instance of the class
MFRC522::MIFARE_Key key;

/* Set the block to which we want to write data */
/* Be aware of Sector Trailer Blocks */
int blockNum = 2;
/* Create an array of 16 Bytes and fill it with data */
/* This is the actual data which is going to be written into the card */
byte blockData [16] = {"Himanshu_Sharma"};

/* Create another array to read data from Block */
/* Legthn of buffer should be 2 Bytes more than the size of Block (16 Bytes) */
byte bufferLen = 18;
byte readBlockData[18];

MFRC522::StatusCode status;

void setup()
{
/* Initialize serial communications with the PC */
Serial.begin(9600);
/* Initialize SPI bus */
SPI.begin();
/* Initialize MFRC522 Module */
mfrc522.PCD_Init();
Serial.println("Scan a MIFARE 1K Tag to write data...");
}

void loop()
{
/* Prepare the ksy for authentication */
/* All keys are set to FFFFFFFFFFFFh at chip delivery from the factory */
for (byte i = 0; i < 6; i++)
{
key.keyByte[i] = 0xFF;
}
/* Look for new cards */
/* Reset the loop if no new card is present on RC522 Reader */
if ( ! mfrc522.PICC_IsNewCardPresent())
{
return;
}

/* Select one of the cards */
if ( ! mfrc522.PICC_ReadCardSerial())
{
return;
}
Serial.print("\n");
Serial.println("**Card Detected**");
/* Print UID of the Card */
Serial.print(F("Card UID:"));
for (byte i = 0; i < mfrc522.uid.size; i++)
{
Serial.print(mfrc522.uid.uidByte[i] < 0x10 ? " 0" : " ");
Serial.print(mfrc522.uid.uidByte[i], HEX);
}
Serial.print("\n");
/* Print type of card (for example, MIFARE 1K) */
Serial.print(F("PICC type: "));
MFRC522::PICC_Type piccType = mfrc522.PICC_GetType(mfrc522.uid.sak);
Serial.println(mfrc522.PICC_GetTypeName(piccType));

/* Call 'WriteDataToBlock' function, which will write data to the block */
Serial.print("\n");
Serial.println("Writing to Data Block...");
WriteDataToBlock(blockNum, blockData);

/* Read data from the same block */
Serial.print("\n");
Serial.println("Reading from Data Block...");
ReadDataFromBlock(blockNum, readBlockData);
/* If you want to print the full memory dump, uncomment the next line */
//mfrc522.PICC_DumpToSerial(&(mfrc522.uid));

/* Print the data read from block */
Serial.print("\n");
Serial.print("Data in Block:");
Serial.print(blockNum);
Serial.print(" --> ");
for (int j=0 ; j<16 ; j++)
{
Serial.write(readBlockData[j]);
}
Serial.print("\n");
}

void WriteDataToBlock(int blockNum, byte blockData[])
{
/* Authenticating the desired data block for write access using Key A */
status = mfrc522.PCD_Authenticate(MFRC522::PICC_CMD_MF_AUTH_KEY_A, blockNum, &key, &(mfrc522.uid));
if (status != MFRC522::STATUS_OK)
{
Serial.print("Authentication failed for Write: ");
Serial.println(mfrc522.GetStatusCodeName(status));
return;
}
else
{
Serial.println("Authentication success");
}

/* Write data to the block */
status = mfrc522.MIFARE_Write(blockNum, blockData, 16);
if (status != MFRC522::STATUS_OK)
{
Serial.print("Writing to Block failed: ");
Serial.println(mfrc522.GetStatusCodeName(status));
return;
}
else
{
Serial.println("Data was written into Block successfully");
}

}

void ReadDataFromBlock(int blockNum, byte readBlockData[])
{
/* Authenticating the desired data block for Read access using Key A */
status = mfrc522.PCD_Authenticate(MFRC522::PICC_CMD_MF_AUTH_KEY_A, blockNum, &key, &(mfrc522.uid));

if (status != MFRC522::STATUS_OK)
{
Serial.print("Authentication failed for Read: ");
Serial.println(mfrc522.GetStatusCodeName(status));
return;
}
else
{
Serial.println("Authentication success");
}

/* Reading data from the Block */
status = mfrc522.MIFARE_Read(blockNum, readBlockData, &bufferLen);
if (status != MFRC522::STATUS_OK)
{
Serial.print("Reading failed: ");
Serial.println(mfrc522.GetStatusCodeName(status));
return;
}
else
{
Serial.println("Block was read successfully");
}

}

Card Reading Code :

#include <SPI.h>
#include <MFRC522.h>
#include <Servo.h>

#define SS_PIN 10
#define RST_PIN 9

//#define SERVO_PIN 3
//Servo myservo;

#define ACCESS_DELAY 2000
#define DENIED_DELAY 1000
MFRC522 mfrc522(SS_PIN, RST_PIN); // Create MFRC522 instance.

void setup()
{
 Serial.begin(9600); // Initiate a serial communication
 SPI.begin(); // Initiate SPI bus
 mfrc522.PCD_Init(); // Initiate MFRC522

//myservo.attach(SERVO_PIN);
//myservo.write( 70 );
//delay(7500);
//myservo.write( 0 );
 Serial.println("Put your card to the reader...");
 Serial.println();
}
void loop()
{
 // Look for new cards
 if ( ! mfrc522.PICC_IsNewCardPresent())
 {
  return;
 }
 // Select one of the cards
 if ( ! mfrc522.PICC_ReadCardSerial())
 {
  return;
  }
//Show UID on serial monitor
Serial.print("UID tag :");
String content= "";
byte letter;
for (byte i = 0; i < mfrc522.uid.size; i++)
{
 Serial.print(mfrc522.uid.uidByte[i] < 0x10 ? " 0" : " ");
 Serial.print(mfrc522.uid.uidByte[i], HEX);
 content.concat(String(mfrc522.uid.uidByte[i] < 0x10 ? " 0" : " "));
 content.concat(String(mfrc522.uid.uidByte[i], HEX));
 }
 Serial.println();
 Serial.print("Message : ");
 content.toUpperCase();
 if (content.substring(1) == "69 C8 E2 2A") //change here the UID of the card
 {
 Serial.println("Authorized access");
 Serial.println();
 //myservo.write( 70 );
 //delay(7500);
 //myservo.write( 0 );
 }
 else {
 Serial.println(" Access denied");
 delay(DENIED_DELAY);
}
}